Backup the existing application software

Select Backup (F3) (double click) from the desktop, you will be prompted for a password the password is manager.

Enter password “manager” (do not include quotes) and click ok.

After the password is accepted, the following window will appear.

Insert one of the blank Zip disks into the Zip drive installed in the NT computer.

Zip Drive

If at any time you feel the need to abort the copy procedure press the Ctrl key and the “C” key at the same time.

Wait approximately 30 seconds for the drive to initialize and press a key to continue during the backup procedure you should see the backup window fill up with copy messages as shown below.

Note: Some files take longer to copy than others; it’s not unusual for a file to take 60 seconds to copy.

Note: Actual Window will be KDF Application Backup, Actual text displayed will vary.

When the copy procedure is done the Backup window will close. Remove the Zip disk and label with the system serial number, data, your initials and the text upgrade backup.

Backup the Recipe Files:

It is not necessary to backup recipe files – they are part of the system backup