## Slide 1: Preclinical Imaging: MRI Basic Safety Training

## Slide 2: MRI Introduction
MRIs are an imaging technique that uses magnetic fields, gradients, and radio waves to take pictures of the anatomy and physiological processes inside the body.
MRIs are noninvasive and radiation-free!
Used as diagnostic and research tools.

## Slide 3: Personnel Safety
Because MRIs use powerful magnets, it is important to be:
Medically safe
Medically cleared by a trained operator
Physically safe
Remove all items on person
Place all items in designated bins
Vigilant to keep others safe
Understand risks and watch out for others

## Slide 4: Metals
Ferrous/Ferromagnetic: Iron, steel, some stainless steel, nickel
  Are attracted to the magnet
Paramagnetic: Gold, silver, platinum, titanium, aluminum, copper, brass, and lead
  Can have induced magnetic forces
General Rule: Keep Metal Items Out!

## Slide 5: Equipment Safety
New items must be cleared by trained staff before bringing into the Magnet Room
Prevent any unknown items from entering the Magnet Room!
REMEMBER: The MRI IS ALWAYS ON!

## Slide 6: Facility Hazards To Be Aware Of
Preclinical Imaging and NMR share the same space
Magnetic Field Hazards
  Always ON!
  There are barrier-less magnet zones so walking outside of designated paths are unsafe
Cryogenic Hazards
  Asphyxiation (nitrogen 695:1 helium 760:1)
  Frostbite (nitrogen -196C helium -269C)
  Chemical Explosions
Chemical Hazards
  Potentially Toxic and Dangerous compounds and solvents

## Slide 7: Facility Zones

## Slide 8: Zone 1: Public Areas
Elevators
Restrooms
ISTB1 Lobby

## Slide 9: Zone 2: Low-Risk
Break area
Staff Offices
ISTB1 L2 Pathways outside of facility to and from elevators/stairwells

## Slide 10: Zone 3: Trained Staff
Untrained Students/Visitors Must Have Permission from Proper Channels, Briefed On Hazards, & Screened
MR Computer & Bench Stations
Areas Just Outside Of Magnet Zones

## Slide 11: Zone 4: High Risk
Magnet Zones
Restricted To Trained Staff Only
Keep belongings And Unauthorized Items Out!
Ferrous Metals Brought Here Pose A Huge Danger!

## Slide 12: No Food or Drink Area

## Slide 13: Important Takeaways
The MRI Is ALWAYS ON!
  Be Vigilant!
General Rule: Keep ALL Metal Items OUT!
  Ferrous = Attracted To Magnet
  Remove Belongings Before Entering The Magnet Room
  Check New Items With Staff
Review Facility Zones
  Follow Designated Paths
  Be aware of the areas you enter
HAVE FUN! STAY SAFE!
Safety Certification Guide:
MRI Safety Instructions
MR Medical Screening Form
Magnet Safety Test
Facility Walkthrough